SP-SDIX2

3G/HD-SDI 1 x 2

High Bandwidth

Distribution Amplifier

User manual

All Rights Reserved VER: 1.1

Thank you for purchasing this product. For optimum performance and safety, please read these instructions carefully before connecting, operating or adjusting this product. Please keep this manual for future reference.

I. Introduction

The KanexPro 1x2 SDI unit can split, re-clock, and amplify SDI source video to 2 SDI outputs providing full HD 1080p resolution to up to 2 displays simultaneously for faster broadcasting and production.

II. Features

- Distribute one SDI input to four SDI displays/ monitors

- Supports SD-SDI (270Mb/s), HD-SDI (1.485Gb/s), 3G-SDI (2.97Gbps) video format.

- Built-in cable equalization and re-clocking

- HD resolutions up to 1920x1080@60Hz.

- Supports signal input and output distances of up to 300m for SD signals, 200m for HD signals and 100m for 3G signals.

- Supports 5-12V wide voltage input.

III. Package

- 1x2 SDI Splitter --------------------------------------------------------------------------- 1

- 5V1A DC Power Supply adapter ------------------------------------------------------- 1

- Operation Manual ------------------------------------------------------------------------- 1

IV. Specifications

- Frequency Bandwidth                3Gbps

- SDI Splitter Input Ports               1 x BNC Female input port

- SDI Splitter Output Ports              2 x BNC Female output ports

- Power Supply                       DC 5V 1A

- ESD Protection Human Body Model:    ± 8kV (air-gap discharge)

± 4kV (contact discharge)

- Dimensions (mm)                   70(W) X 145 (D) X 25 (H)

- Weight                            320g

- Operating Temperature	              0°C ~ 40°C / 32°F ~ 104°F

- Storage Temperature	             -20°C ~ 60°C / -4°F ~ 140°F

- Relative Humidity                  20 ~ 90% RH (Non-condensing)

- Power Consumption (Max) 	       1.5W

V. Operation controls and Functions

Front Panel

- ON/OFF: Power on/off switch.

- POWER LED: This red LED illuminate when the device is connected with power supply.

- LOCK LED: This red LED illuminate when the SDI signal plug in.

Rear Panel

- SDI INPUT: This slot is where you connect the SDI source output from SDI Camera.

- SDI OUTPUT: These slots are where you connect the SDI displays or monitors with coaxial cable (RG6).

- DC 5V-12V: Plug the 5V or 12V DC power supply into the unit and connect the adapter to AC wall outlet.

VI. Application Example

For Technical Support: Email to our after-sales department or make a call, please inform us the following information about your cases.

- Product version and name.

- Detailed failure situations.

- The formation of the cases.

Please Contact KanexPro directly at 888-975-1368 or email us at support@kanexpro.com.

Model: SP-SDIX2